City of Sadieville

P.O. Box 129, 605 Pike Street

Sadieville, Kentucky  40370

Phone: (502) 857-4576; Fax: (502) 857-4555

Email:  sadievilleky@bellsouth.net

# Main Street Stone Wall Restoration Specifications

$1,000,000 Liability Insurance and Worker’s Comp Required

Approximate Area:

~387 sq.ft.

129 Lf.

The purpose of this project is to reinforce/stabilize the existing crumbling cinderblock wall located on Main street in front of 205-207 Main St. Sadieville KY 40370. In addition to Reinforcement/Stabilization there would be:

- ADA Compliant Handicap access ramp with handrail (Supplied by Contractor) to be installed at the end of the sidewalk located at the entrance to Johnson Alley

- Stacked stone, Stone Veneer or similar applied to the façade with cap stones

- Ensure proper drainage and weatherboard lapping

- Project would need to commence and be completed within 60 days of acceptance of bid

- Street, Parking lot and sidewalk surfaces will be protected from damage caused by construction activity

The following repairs need to be completed by contractor prior to stone work.

- Any damaged cinder blocks need to be repaired or replaced.

- Inspect, repair and install any new or existing damaged drains .

- Repair or replace any loose material to allow stone attachment.

- Contractor will supply all materials and equipment required to complete the job.

- Stone is to match existing style of the dry stacked stone walls in the area.

- All building signage to be removed prior to painting and reinstalled to its current location after painting.

- Concrete/ Morter shall be allowed to cure before any sealants are applied

**Bids are required to be turned in by Friday, October 3rd, 2020 by 5:00PM to Sadieville City Hall to be considered. Job will be awarded Monday, October 5th, 2020 at a special city meeting to be held at City Hall at 10:00 AM